TYPE INSPECTION REPORT

Part 1 – Airplane Ground Inspection

# INSTRUCTIONS

| This form is to be used to record the results of conformity inspections and investigations of prototype or modified airplane presented for type certification. Many inspections and tests will be witnessed or participated in which are not covered by questions listed herein. All such inspections and tests and changes to the product and/or type design data resulting therefrom must be recorded and made a part of this report. This form includes references to applicable RBHA. Some sections are interrelated, and future RBHA revision may modify the requirement of an item. It is essential that the specific RBHA’s applicable to the airplane involved be reviewed to insure a complete and effective inspection. When this form is used in conjunction with a program which involves an airplane being certificated under a CAR, cross out the RBHA reference and enter the equivalent CAR reference. All entries must be clear, concise, and self-explanatory. Answer questions in this report by checking the appropriate “YES” or “NO” column. When action is required to render the item acceptable, check “ACTION REQ.” Use additional pages to list the unsatisfactory conditions found during the inspection with reference to any communication or conformity inspection reports relative to the item. Number the pages with the page number on which the question appears plus a letter, i.e., 10a, 10b, etc. Identify the unsatisfactory condition by using the related item number as it appears on the form; list numerically with sufficient space between each entry to note the corrective action taken. When the item has been reinspected, cross out the previous “NO” answer and enter the new answer. This will be done for each inspection until the item is acceptable and will serve as a record of the number of times the item was inspected prior to acceptance. |  | When a question is not applicable to the product being inspected, enter “NA” across the “YES” and “NO” columns denoting not applicable. Pages containing only inapplicable questions may be omitted. Indicate by page numbers in the space provided on page 1, the pages submitted (or pages omitted if more convenient) in this report. When more than one inspector participates in completing a report, each will enter his signature and title on page 1. He will also insert his initials adjacent to the answers and determinations he provides within the report. The applicant’s weight and balance report may be used in lieu of the weight and dimensional page of this form provided it contains all the information requested. An equipment list with enough copies for each copy of the type inspection report submitted, setting forth, where pertinent, the make, model, and serial number of each item, must be attached as part of the report. When any part of the list is part of the weight and balance report, the weight of each item and the horizontal distance from the datum line will be shown. This list should include only significant items or accessories; i.e., those of a type that could have an adverse effect on the airworthiness or operational characteristics of the airplane if replaced by other items the acceptability of which have not been determined. For example, this list should include, but not necessarily be limited to, seats, safety belts, fire extinguishers, electronic equipment, electric motors, instruments, wheels and brakes, tires, skis, floats, superchargers, heaters, engines, starters, generators, etc. When concerned with alteration of airplane under the supplemental type certification program, it is especially important to consider this list. |
| --- | --- | --- |

| EXAMPLE: | YES | NO | ACTION REQ. |
| --- | --- | --- | --- |
|  |  | ( | X |
|  |  | ( |  |
|  | X |  |  |

DO NOT SUBMIT THIS PAGE WITH REPORT

Reports Identification: ERJ 190

| TYPE INSPECTION REPORT Part 1 – AIRPLANE GROUND INSPECTION | AGÊNCIA NACIONAL DE AVIAÇÃO CIVIL Gerência Geral de Certificação de Produtos Aeronáuticos | TIA |
| --- | --- | --- |
|  |  | NO. |  |
|  |  | DATED |  |
| APPLICANT | NAME |  | ADDRESS (Number, street, city, State, and ZIP code) |
| AIRPLANE | MODEL |  | DATA SHEET NO. | DATED |
|  | SERIAL NUMBERS |  |  |  |  |  |  |
|  | REGISTRA- TION MARKS |  |  |  |  |  |  |
| BASIS FOR CERTIFICATION | RBHA PART | DATED | AMENDMENTS |
| MODIFIED BY | NAME | ADDRESS (Number, street, city , State, and ZIP code) |
| DESCRIPTION OF ALTERATION |
| PAGES | ( | (SUBMITTED (OMITTED | ( | IN THIS REPORT |
| ATTACHMENTS |
| INSPECTIONS CONDUCTED BY (Name and identification) |
| PREPARED | DATE | BY (Title and signature) |
| REVIEWED |  |  |
| APPROVED |  |  |

TABLE OF CONTENTS

| ITEM | TITLE | PAGE |
| --- | --- | --- |
|  | Cover Sheet | 1 |
|  | Table of Contents | 2 |
|  | Administrative Data | 3 |
| 1.0 | Empty Weight and C.G. Location | 4 |
| 2.0 | Fabrication Processes | 5 |
| 3.0 | Inspection – General | 6 |
| 4.0 | Airframe | 7 |
| 4.1 | General | 7 |
| 4.2 | Fuselage | 7 |
| 4.3 | Wing | 8 |
| 4.4 | Empennage | 9 |
| 5.0 | Flight Control System | 10-12 |
| 6.0 | Landing Gear | 13 |
| 6.1 | General | 13 |
| 6.2 | Landing Gear Installation | 13 |
| 6.3 | Ski Installation | 13 |
| 6.4 | Float Installation | 13 |
| 7.0 | Personnel and Cargo Accommodations | 14-16 |
| 8.0 | Ventilation, Heating and Pressurization | 17 |
| 9.0 | Fire Protection – Compartment Interior | 18 |
| 10.0 | Powerplant Installation | 19 |
| 10.1 | General | 19 |
| 10.2 | Fuel System | 19-21 |
| 10.3 | Oil System | 21-22 |
| 10.4 | Induction System | 22 |
| 10.5 | Exhaust System | 22 |
| 10.6 | Controls and Accessories | 23 |
| 10.7 | Fire Protection | 23-24 |
| 11.0 | Equipment | 25-27 |
| 12.0 | Electrical System and Equipment | 28 |
| 13.0 | Safety Equipment | 28 |
| 14.0 | Miscellaneous Equipment | 29 |
| 14.1 | Electronic System | 29 |
| 14.2 | Hydraulic and Pneumatic System | 29 |
| 14.3 | Oxygen System | 30 |
| 14.4 | Miscellaneous Fluid Drains | 31 |
| 15.0 | Aircraft Identification and Marking | 31 |
| 16.0 | Software System | 31-32 |

| ADMINISTRATIVE DATA |
| --- |
| A. INSPECTION PERIOD | B. WHERE INSPECTION CONDUCTED |
| FROM | TO |  |
| FORM SUBMITTED BY APPLICANT |  | STATEMENT OF CONFORMITY | DATED |
|  |  | MAJOR REPAIR AND ALTERATION FORM | DATED |
|  | YES | NO |
| DOES THE APPLICANT’S INSPECTION SYSTEM ASSURE THAT THE MATERIALS AND PARTS USED IN THE PROTOTYPE AIRCRAFT ARE IN CONFORMITY WITH APPROVED DATA |  |  |
| DOES THE APPLICANT MAINTAIN RECORDS OF THE INSPECTION CONDUCTED ON THE PROTOTYPE TO SUBSTANTIATE HIS STATEMENT OF CONFORMITY |  |  |
| NUMBER OF CTA CONFORMITY INSPECTIONS | G. NUMBER OF UNSATISFACTORY ITEMS |
| CONDUCTED | RECORDED IN PROJECT FILE | RECORDED IN THIS REPORT |
| H. DESCRIPTION OF AIRCRAFT INSPECTED |
| REMARKS |

| 1. ACTUAL EMPTY WEIGHT AND CENTER OF GRAVITY LOCATION |
| --- |
| 1.1 Leveling means (RBHA 23.871, RBHA 25.871) |
| 1.2 Location of datum |
| 1.3 Required prior to weighing (RBHA 23.29, RBHA 25.29) |
| VOLUME (Gals.) | FIXED BALLAST | UNUSABLE FUEL | UNDRAINABLE OIL | ENGINE COOLANT | HYDRAULIC FLUID |
| WEIGHT (Lbs.) |  |  |  |  |  |
| Actual empty weight | SCALE POINTS | WEIGHT (lb) | HORIZONTAL DISTANCE FROM DATUM (Inches) | MOMENT (Inch – lb) |
|  | FORWARD LEFT |  |  |  |
|  | FORWARD RIGHT |  |  |  |
|  | REAR LEFT |  |  |  |
|  | REAR RIGHT |  |  |  |
|  | AUXILIARY |  |  |  |
|  | TOTAL |  |  |  |
| forward 1.3.2 Empty weight c.g. is _____________ inches aft of datum |
| 1.3.3 Aircraft weighed conformed to | AIRCRAFT WEIGHT (Mfgs. Serial No.) |
| DRAWING LIST NO. | DATED | EQUIPMENT LIST NO. | DATED |  |

TIA FINDINGS Record results of investigations and special tests, such as static, endurance, operational, pressure, functional, and reliability, conducted or witnessed by manufacturing inspectors on the basis of instructions contained in item 18 of the type inspection authorization. Identify by TIA item number and item description; results to follow directly below the item description.

| 2.0 FABRICATION PROCESSES | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 2.1 | Have the chemical and physical properties of materials used in the fabrication of major and/or critical parts been satisfactorily substantiated to assure conformity with material requirements of the related data RBHA 21.33 23.605 25.605 |  |  |  |
| 2.2 | Has the heat treatment of major and/or critical parts been adequately controlled to assure the fabrication of these parts in accordance with pertinent requirements of approved data RBHA 21.33 23.605 25.605 |  |  |  |
| 2.3 | Has welding, brazing, and normalizing of major and/or critical parts been adequately controlled to assure fabrication of these parts in accordance with pertinent requirements of the approved data RBHA 21.33 23.605 25.605 |  |  |  |
| 2.4 | Have special techniques, (i.e., structural shotpeening etching, etc.) on major and/or critical parts been adequately controlled to assure fabrication of these parts in accordance with pertinent requirements of the approved data RBHA 21.33 23.605 25.605 |  |  |  |
| 2.5 | Have special forming processes (explosive, magnetic, etc.) on major and/or critical parts been adequately controlled to assure processing according to related specifications and fabrications in according with pertinent requirements of the approved data RBHA 21.33 23.605 25.605 |  |  |  |
| 2.6 | Have processes for manufacturing or forming of special materials (i.e., plastics, phenolics, fiberglass, etc.) for major and/or critical parts been adequately controlled to assure fabrication of these parts in accordance with pertinent requirements of the approved data RBHA 21.33 23.605 25.605 |  |  |  |
| 2.7 | Has application of protective treatments to major and/or critical parts been adequately controlled to assure conformity with pertinent requirements of the approved data RBHA 21.33 23.605 25.605 |  |  |  |
| 2.8 | Have processes for bonding or gluing of major and/or critical parts been adequately controlled to assure the fabrication of these parts in accordance with pertinent requirements of the approved data RBHA 21.33 23.605 25.605 |  |  |  |
| 2.9 | Have processes for sealing and finishing of major and/or critical parts been adequately controlled to assure conformity with pertinent requirements of the approved data RBHA 21.33 23.605 25.605 |  |  |  |
| 2.10 | List, by specification or drawing number, any special process or fabrication method used that is not covered in this section. |

| 3.0 INSPECTION - GENERAL | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 3.1 | Are drawings, specifications, equipment lists and other type design data available for inspection of the prototype product RBHA 21.33 23.605 25.605 |  |  |  |
| 3.2 | Has a method been established to update these data to show the latest type design changes RBHA 21.33 23.605 25.605 |  |  |  |
| 3.3 | Has a method been established to show the status of these changes relative to the prototype article and parts thereof RBHA 21.33 23.605 25.605 |  |  |  |
| 3.4 | Are deviations from the type design data being recorded RBHA 21.33 23.605 25.605 |  |  |  |
| 3.5 | Are parts and assemblies properly stamped, marked or otherwise identified to indicate the inspection status during various stages of fabrication RBHA 21.33 23.605 25.605 |  |  |  |
| 3.6 | Does inspection of procured items show that they are in conformity with the vendor’s drawings and/or the applicant’s specification drawings RBHA 21.33 23.605 25.605 |  |  |  |
| 3.7 | Have critical castings received 100 percent inspection by visual, radiographic, and magnetic particular penetrant inspection or approved equivalent nondestructive inspection methods RBHA 23.621 …… 25.621 |  |  |  |
| 3.8 | Have noncritical castings been inspected in accordance with the following table: RBHA 23.621 25.621 |  |  |  |
| CASTING FACTOR | INSPECTION |  |  |  |
| (a) 2.0 or more | 100 percent visual |  |  |  |
| Less than 2.0 but More than 1.5 | 100 percent visual and magnetic particle or penetrant or equivalent nondestructive inspection methods |  |  |  |
| (c) 1.25 through 1.50 | 100 percent visual, magnetic particle or penetrant, and radiographic or approved equivalent nondestructive inspection methods |  |  |  |
| REMARKS |

| 4.0 AIRFRAME | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 4.1 | GENERAL |  |  |  |
| 4.1.1 | Are nonmetallic external components protected against erosion RBHA 23.609 25.609 |  |  |  |
| 4.1.2 | Have adequate drainage provisions been provided to prevent the accumulation of fuel, water, hydraulic oil, etc. RBHA 23.609 25.609 |  |  |  |
| 4.1.3 | Have adequate ventilation provisions been provided to prevent the accumulation of fumes, smoke, gases, etc. RBHA 23.609 25.609 |  |  |  |
| 4.1.4 | Have all members of the structure been suitably protected against deterioration or loss of strength in service due to weathering, corrosion, abrasion, etc. RBHA 23.609 25.609 |  |  |  |
| 4.1.5 | Have adequate inspection openings, doors, and access panels been provided to allow close examination of each part requiring recurring inspection, adjustments for proper alignment and function, or lubrication RBHA 23.611 25.611 |  |  |  |
| 4.2 | FUSELAGE |  |  |  |
| 4.2.1 | Have rivets been driven in accordance with acceptable standards RBHA 23.603, .605 25.605 |  |  |  |
| 4.2.2 | Have bolts been installed in accordance with acceptable standards with respect to proper length, washers, nuts, hole size, finish, etc. RBHA 23.603, .605 25.605 |  |  |  |
| 4.2.3 | Are self-locking nuts used on any bolt subject to rotation during aircraft operation RBHA 23.607 25.607 |  |  |  |
| 4.2.4 | Do detail parts fit into subassemblies without being forced or sprung RBHA 23.603, .605 25.605 |  |  |  |
| 4.2.5 | Do subassemblies fit the fuselage assembly without being forced or sprung RBHA 23.603, .605 25.605 |  |  |  |
| 4.2.6 | Are major attachment points of the wing, empennage, landing gear, powerplant, etc., adequately controlled to insure proper alignment when mated RBHA 23.603, .605 25.605 |  |  |  |
| 4.2.7 | Are structural panels such as bulkhead, spar and beam webs, and outside skin panel covering, free from buckles or wrinkles RBHA 23.603, .605 25.605 |  |  |  |
| 4.2.8 | Do doors, hatches, etc., fit and operate properly RBHA 23.603, .605 25.605 |  |  |  |
| 4.2.9 | Are there any questionable design items RBHA 23.601 25.601 |  |  |  |

| 4.0 AIRFRAME (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 4.3 | WINGS |  |  |  |
| 4.3.1 | Have rivets been driven in accordance with acceptable standards RBHA 23.603, .605 25.605 |  |  |  |
| 4.3.2 | Have bolts been installed in accordance with acceptable standards with respect to proper length, washers, nut, hole size, finish, etc. RBHA 23.603, .605 25.605 |  |  |  |
| 4.3.3 | Are self-locking nuts used on any bolt subject to rotation during aircraft operation RBHA 23.607 25.607 |  |  |  |
| 4.3.4 | Do detail parts fit into subassemblies without being forced or sprung RBHA 23.603, .605 25.605 |  |  |  |
| 4.3.5 | Do subassemblies fit the wing assembly without being forced or sprung RBHA 23.603, .605 25.605 |  |  |  |
| 4.3.6 | Are major attachment points of tabs, flaps, ailerons, slats, spoilers, landing gear and fuselage adequately controlled to insure proper alignment when assembled to corresponding structure RBHA 23.603, .605 25.605 |  |  |  |
| 4.3.7 | Are structural panels such as spar webs, rib webs, and skin panels, free from buckles or wrinkles RBHA 23.603, .605 25.605 |  |  |  |
| 4.3.8 | Are adequate inspection openings, doors or access panels been provided to allow close examination of each part requiring recurring inspection, adjustments for proper alignment and function, or lubrication RBHA 23.611 25.611 |  |  |  |
| 4.3.9 | Has wing alignment been properly controlled RBHA 23.603, .605 25.605 |  |  |  |
| 4.3.10 | Do the hinge lines of the ailerons, spoilers, slats, flaps, tabs, etc., match properly when installed RBHA 23.603, .605 25.605 |  |  |  |
| 4.3.11 | Is there positive clearance between the wing and all moveable surfaces throughout their range of operation RBHA 23.683 25.683 |  |  |  |
| 4.3.12 | Are the flight control surface operating means (i.e.. bell cranks, push-pull tubes, chains, cables, operating cylinders, jackscrews, etc.) free from binding and interference RBHA 23.683 25.685 |  |  |  |
| 4.3.13 | Are positive stops provided to limit the range of motion of the flight control surfaces RBHA 23.675 25.675 |  |  |  |
| 4.3.14 | Are adequate ventilation and drainage provisions provided for the wing and all control surfaces or lift augmentation devices RBHA 23.609 25.609 |  |  |  |
| 4.3.15 | Are there any questionable design items RBHA 23.601 25.601 |  |  |  |
| 4.3.16 | Is the balance of all control surfaces within the drawing tolerances RBHA 23.671 25.671 |  |  |  |

| 4.0 AIRFRAME (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 4.4 | EMPENNAGE |  |  |  |
| 4.4.1 | Have rivets been driven in accordance with acceptable standards RBHA 23.605 25.605 |  |  |  |
| 4.4.2 | Have bolts been installed in accordance with acceptable standards with respect to proper length, washers, nuts, hole size, finish, etc. RBHA 23.605 25.605 |  |  |  |
| 4.4.3 | Are self-locking nuts used on any bolt subject to rotation during aircraft operation RBHA 23.607 25.607 |  |  |  |
| 4.4.4 | Do Detail parts fit into subassemblies without being forced or sprung RBHA 23.603, .605 25.605 |  |  |  |
| 4.4.5 | Do subassemblies fit the empennage assembly without being forced or sprung RBHA 23.603, .605 25.605 |  |  |  |
| 4.4.6 | Are major attachment points of tabs, elevator, rudder, horizontal and vertical stabilizer adequately controlled to insure proper alignment when assembled to corresponding structure RBHA 23.603, .605 25.605 |  |  |  |
| 4.4.7 | Are structural panels such as spar webs, rib webs, skin panels, etc., free from buckles or wrinkles RBHA 23.603, .605 25.605 |  |  |  |
| 4.4.8 | Are adequate inspection opening, doors, and/or access panels provided to allow close examination of each part requiring recurring inspection, adjustments for proper alignment and function, or lubrication RBHA 23.611 25.611 |  |  |  |
| 4.4.9 | Has horizontal and vertical stabilizer alignment been properly controlled RBHA 23.603, .605 25.605 |  |  |  |
| 4.4.10 | Do the hinge lines of the elevator, rudder and tabs match properly when installed RBHA 23.603, .605 25.605 |  |  |  |
| 4.4.11 | Is there positive clearance between the vertical or horizontal stabilizer, and all movable surfaces throughout their range of operation RBHA 3.683 25.683 |  |  |  |
| 4.4.12 | Are the flight control surface operating means (i.e.., bell cranks, push-pull tabs, chains, cables, operating cylinders, jackscrews, etc.) free from binding and interference RBHA 23.685 25.685 |  |  |  |
| 4.4.13 | Are positive stops provided to limit the range of motion of the rudder, elevator and stabilizer (when an adjustable stabilizer is employed) RBHA 23.675 25.675 |  |  |  |
| 4.4.14 | Are adequate drainage provisions provided for the empennage FAR 23.609 25.609 |  |  |  |
| 4.4.15 | Are there any questionable design items RBHA 27.601 29.601 |  |  |  |
| 4.4.16 | Is the balance of all control surfaces within the drawing tolerances RBHA 23.671 25.671 |  |  |  |

| 5.0 FLIGHT CONTROL SYSTEM | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 5.1 | Do all flight controls operate with ease, smoothness and positiveness throughout their maximum limits RBHA 23.671 25.671 |  |  |  |
| 5.2 | Do all flight control surfaces move in the correct direction of travel in response to operation of the cockpit controls RBHA 23.779, .671 25.779, .671 |  |  |  |
| 5.3 | Are stops provided for all flight control surfaces and is there positive engagement to limit the control surface travel RBHA 23.675 25.675 |  |  |  |
| 5.4 | Is each element of each flight control system designed, or distinctively and permanently marked, to minimize the probability of incorrect assembly that could result in the malfunctioning of the system RBHA 23.685 25.685 |  |  |  |
| 5.5 | Where cable systems are used, are provisions provided for the visual inspection of fairleads, pulleys, terminals and turnbuckles RBHA 23.689 25.689 |  |  |  |
| 5.6 | Is there a means provided, adjacent to the trim control, to indicate the direction of the airplane motions RBHA 23.677 25.677 |  |  |  |
| 5.7 | Is there provided a clearly visible means to indicate the position of the trim device with respect to the range of adjustment RBHA 23.677 25.677 |  |  |  |
| 5.8 | Where irreversible trim tab control systems are used. Is the aprt from the tab to the attachment of the irreversible unit to the airplane structure rigid RBHA 23.677 25.677 |  |  |  |
| 5.9 | Does a functional check show that the control system locks operate as placarded or marked RBHA 23.679 25.679 |  |  |  |
| 5.10 | Has a means been provided to prevent the control system lock from engaging in flight RBHA 23.679 25.679 |  |  |  |
| 5.11 | Is the flight control system free from jamming, excessive friction. And excessive deflection when the controls are operated from the pilot compartment with: |  |  |  |
|  | The system loaded to correspond to 80 percent of the limit load specified for the system RBHA 25.683 |  |  |  |
|  | (b) The system loaded to correspond to the limit air loads on the appropriate surfaces RBHA 23.683 |  |  |  |
| 5.12 | Is the control system protected from jamming, chafing and interference by cargo, passengers, or loose objects RBHA 23.685 25.685 |  |  |  |

| 5.0 FLIGHT CONTROL SYSTEM (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 5.13 | Are means provided in the cockpit to prevent the entry of foreign objects into places where they would jam the control system RBHA 23.685 25.685 |  |  |  |
| 5.14 | Are means provided to prevent the slapping of cables or tubes against other parts RBHA 23.685 25.685 |  |  |  |
| 5.15 | Are the control pulleys provided with guards to prevent the cables from being misplaced or fouled RBHA 23.689 25.689 |  |  |  |
| 5.16 | Do the control pulleys lie in a plane passing through the cable so that the cable does not rub against the pulley flange RBHA 23.689 25.689 |  |  |  |
| 5.17 | Are there any fairlead installations which change the cable direction more than 3 degrees RBHA 23.689 25.689 |  |  |  |
| 5.18 | Are there any clevis pins in the control system subject to load or motion which are retained only by cotter pins RBHA 23.689 25.689 |  |  |  |
| 5.19 | Are turnbuckles and push rods attached to parts having angular motion in a manner that will positively prevent binding or bending throughout the range of travel RBHA 23.689 25.689 |  |  |  |
| 5.20 | When the flap control is placed in any selected operational position, will the flap remain in that position unless the control is adjusted RBHA 23.697 25.697 |  |  |  |
| REMARKS |

| 5.0 FLIGHT CONTROL SYSTEM (Continued) |
| --- |
| 5.21 | Control Surface Travels NOTE: The applicant’s flight control operational form(s) may be used in lieu of the information requested below if it is considered that it is more pertinent to the system being checked. When other data is used, it should be included as an attachment. |
| A. AT BEGINNING OF CTA OFFICIAL FLIGHT TEST |
| SURFACE | POSITION | ACTUAL MEASURE- MENT (In inches or degrees) | POSITION | ACTUAL MEASURE- MENT (In inches or degrees) | POSITION | ACTUAL MEASURE- MENT (In inches or degrees) | CABLE TENSION (lb)1 |
| WING FLAPS | TAKEOFF |  | APPROACH |  | LAND |  |  |
| AILERON | LEFT HAND | UP |  | DOWN |  |  |  |  |
|  | RIGHT HAND | UP |  | DOWN |  |  |  |  |
| AILERON TRIM TAB | UP |  | DOWN |  |  |  |  |
| AILERON SERVO TAB | LEFT HAND | UP |  | DOWN |  | LAND |  |  |
|  | RIGHT HAND | UP |  | DOWN |  | LAND |  |  |
| SPOILERS | LEFT HAND | UP |  | DOWN |  | LAND |  |  |
|  | RIGHT HAND | UP |  | DOWN |  | LAND |  |  |
| STABILIZER (MOVABLE) | UP |  | DOWN |  |  |  |  |
| ELEVATOR | LEFT HAND | UP |  | DOWN |  |  |  |  |
|  | RIGHT HAND | UP |  | DOWN |  |  |  |  |
| ELEVATOR TRIM TIB | UP |  | DOWN |  |  |  |  |
| ELEVATOR SERVO TAB | UP |  | DOWN |  | LAND |  |  |
| RUDDER | LEFT |  | RIGHT |  |  |  |  |
| RUDDER TRIM TAB | LEFT |  | RIGHT |  |  |  |  |
| RUDDER SERVO TAB | LEFT |  | RIGHT |  | LAND |  |  |
| A. AT BEGINNING OF CTA OFFICIAL FLIGHT TEST |
| SURFACE | POSITION | ACTUAL MEASURE- MENT (In inches or degrees) | POSITION | ACTUAL MEASURE- MENT (In inches or degrees) | POSITION | ACTUAL MEASURE- MENT (In inches or degrees) | CABLE TENSION (lb)1 |
| WING FLAPS | TAKEOFF |  | APPROACH |  | LAND |  |  |
| AILERON | LEFT HAND | UP |  | DOWN |  |  |  |  |
|  | RIGHT HAND | UP |  | DOWN |  |  |  |  |
| AILERON TRIM TAB | UP |  | DOWN |  |  |  |  |
| AILERON SERVO TAB | LEFT HAND | UP |  | DOWN |  | LAND |  |  |
|  | RIGHT HAND | UP |  | DOWN |  | LAND |  |  |
| SPOILERS | LEFT HAND | UP |  | DOWN |  | LAND |  |  |
|  | RIGHT HAND | UP |  | DOWN |  | LAND |  |  |
| STABILIZER (MOVABLE) | UP |  | DOWN |  |  |  |  |
| ELEVATOR | LEFT HAND | UP |  | DOWN |  |  |  |  |
|  | RIGHT HAND | UP |  | DOWN |  |  |  |  |
| ELEVATOR TRIM TIB | UP |  | DOWN |  |  |  |  |
| ELEVATOR SERVO TAB | UP |  | DOWN |  | LAND |  |  |
| RUDDER | LEFT |  | RIGHT |  |  |  |  |
| RUDDER TRIM TAB | LEFT |  | RIGHT |  |  |  |  |
| RUDDER SERVO TAB | LEFT |  | RIGHT |  | LAND |  |  |
| 1. When opposing cables are unequal tension, show tension of each cable and identify. |

| 6.0 LANDING GEAR | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 6.1 | GENERAL |  |  |  |
| 6.1.1 | Is the landing gear structure suitable protected against deterioration or loss of strength in service due to weathering corrosion, abrasion, etc. RBHA 23.609 25.609 |  |  |  |
| 6.1.2 | Are fluid lines, cables and electrical wires and switches attached to the landing gear suitably protected against damage by stones, slush, water, ice, etc. RBHA 23.609 25.609 |  |  |  |
| 6.1.3 | Are self-locking nuts used on any bolt subject to rotation during landing gear operation RBHA 23.607 25.607 |  |  |  |
| 6.1.4 | Are the wheels, brakes, and tires as specified per the related drawings and installed in accordance with this data RBHA 23.731, .733, .735 25.731, .733, .735 |  |  |  |
| 6.2 | LANDING GEAR INSTALLATION |  |  |  |
| 6.2.1 | Did a retractable landing gear operational ground check show proper functioning of the landing gear and landing gear door installations throughout the retraction and extension cycles RBHA 23.729 25.729 |  |  |  |
| 6.2.2 | Did the emergency extension system ground check show proper extension of the landing gear RBHA 23.729 25.729 |  |  |  |
| 6.2.3 | Is a positive means provided to lock the landing gear in the extended position RBHA 23.729 25.729 |  |  |  |
| 6.2.4 | Is a means provided to indicate to the pilot when the landing gear is secured in the extended or retracted position RBHA 23.729 25.729 |  |  |  |
| 6.2.5 | Is an aural warning device provided that functions continuously, when one or more throttles are closed, until the landing gear is down and locked RBHA 23.729 25.729 |  |  |  |
| 6.2.6 | If there is a manual shutoff for the aural warning device, is it installed so that reopening the throttle will reset the warning device RBHA 23.729 25.729 |  |  |  |
| 6.2.7 | Is an aural warning device provided that functions continuously when the wing flaps are extended beyond the maximum approach position RBHA 23.729 25.729 |  |  |  |
| 6.2.8 | Is the equipment that is essential to the safe operation of the airplane and that is located in wheel wells protected from damage by a bursting tire or a loose tire tread RBHA 25.729 |  |  |  |
| 6.3 | SKI INSTALLATION |  |  |  |
| 6.3.1 | Are the skis of an approved type RBHA 23.737 25.737 |  |  |  |
| 6.3.2 | Are the skis, installed in accordance with the approved data RBHA 23.737 25.737 |  |  |  |
| 6.4 | FLOAT INSTALLATION |  |  |  |
| 6.4.1 | Are the floats of an approved type RBHA 23.751 25.751 |  |  |  |
| 6.4.2 | Are the floats installed in accordance with approved data RBHA 23.753 25.753 |  |  |  |

| 7.0 PERSONNEL AND CARGO ACCOMMODATIONS | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 7.1 | Are the windshield and window panels in the pilot compartment clear and free of distortions RBHA 23.773 25.773 |  |  |  |
| 7.2 | Are internal glass panes of a no splintering safety glass RBHA 23.775 25.775 |  |  |  |
| 7.3 | Does the windshield and side windows forward of the pilots back when he is seated in the normal flight position have a luminous transmittance value of not less than 70 percent RBHA 23.775 |  |  |  |
| 7.4 | Are controls and instrument markings, instructions, and placards in conformance with pertinent specifications and approved data |  |  |  |
| RBHA 23.777 through 23.781 25.777 through 25.781 |  |  |  |
| RBHA 23.1541 through 23.1567 25.1541 through 25.1567 |  |  |  |
| 7.5 | Is there a door between the pilot and passenger compartments RBHA 25.771 |  |  |  |
| 7.6 | Does the door, between the pilot and passenger compartment, have a locking means to prevent passengers from opening it without the pilots permission RBHA 25.771 |  |  |  |
| 7.7 | Is there a means to lock and safeguard each external door against inadvertent opening either by persons or as a result of mechanical failure RBHA 25.783 |  |  |  |
| 7.8 | Where inward opening external doors are used, is there a means provided to prevent occupant’s from crowding against the door and interfering with the opening of the door RBHA 25.783 |  |  |  |
| 7.9 | Can the external doors be readily unlocked and opened from the inside or outside RBHA 25.783 |  |  |  |
| 7.10 | Is the means of opening the external doors simple, obvious, and so arranged and marked that they can be readily located and operated, even in darkness RBHA 25.783 |  |  |  |
| 7.11 | Are direct visual inspection means provided to determine whether external doors, for which the initial opening movement is outward, are fully locked RBHA 25.783 |  |  |  |
| 7.12 | Is a visual means provided to signal to appropriate crewmembers when normally used external doors are closed and fully locked RBHA 25.783 |  |  |  |
| 7.13 | Is each seat and berth in accordance with approved data RBHA 25.783 |  |  |  |
| 7.14 | Is each projected object, that would injure persons seated or moving about the airplane in normal flight, padded RBHA 25.785 |  |  |  |

| 7.0 PERSONNEL AND CARGO ACCOMMODATIONS (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 7.15 | Does each berth have an approved safety belt RBHA 25.785 |  |  |  |
| 7.16 | Is there a means provided along each aisle to enable occupants to steady themselves while using the aisles in moderately rough air, such as a hand grip or rail along each aisle or a firm hand hold on each seat back RBHA 25.785 |  |  |  |
| 7.17 | Is each crew member seat at flight deck stations provided with provisions for a shoulder harness RBHA 25.785 |  |  |  |
| 7.18 | Are cargo and baggage compartments placarded in accordance with approved data RBHA 23.787 25.787 |  |  |  |
| 7.19 | Are emergency exits openable from the inside and outside of the cabin without undue effort RBHA 25.809 |  |  |  |
| 7.20 | Is there a means to lock each emergency exit and to safeguard against its opening in flight, either inadvertently by persons or as a result of mechanical failure RBHA 25.809 |  |  |  |
| 7.21 | Is there a means for direct visual inspection of the locking mechanism to determine that each emergency exit, for which the initial opening movement is outward, is fully locked RBHA 25.809 |  |  |  |
| 7.22 | Is each landplane emergency exit that is more than six feet from the ground with the landing gear extended and each over-the-wing emergency exit pro vided with an approved means to assist the occupants in descending to the ground RBHA 25.809 |  |  |  |
| 7.23 | Is each passenger emergency exit, its means of access and its means of opening, conspicuously marked RBHA 23.807 25.811 |  |  |  |
| 7.24 | Is the identity and location of each emergency exit recognizable from a distance equal to the width of the cabin RBHA 25.811 |  |  |  |
| 7.25 | Is the location of each emergency exit operating handle and the instructions for opening marked on or adjacent to the emergency exit RBHA 23.807 25.811 |  |  |  |
| 7.26 | Are these markings and instructions required by item 7.25 readable from a distance of 30 inches RBHA 25.811 |  |  |  |
| 7.27 | Is a source of light, independent of the main lighting system, installed to illuminate each passenger emergency exit marking RBHA 25.811 |  |  |  |

| 7.0 PERSONNEL AND CARGO ACCOMMODATIONS (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 7.28 | Is each emergency exit that is required to be openable from the outside, and its means of opening, marked on the outside of the airplane RBHA 25.811 |  |  |  |
| 7.29 | Are main aisles and emergency access passageways in accordance with approve data RBHA 23.807 25.815, .813 |  |  |  |
| 7.30 | Are the decompression features of personnel and cargo compartments in accordance with approved data RBHA 25.841 |  |  |  |
| 7.31 | Is there any feature or characteristic which may prevent the satisfactory decompression of a compartment RBHA 25.841 |  |  |  |
| REMARKS |

| 8.0 VENTILATION, HEATING AND PRESSURIZATION | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 8.1 | Is the installation of the heating and ventilation system in accordance with related approved data RBHA 21.22 23.831 25.831 |  |  |  |
| 8.2 | Are the heating and ventilation controls placarded and marked in accordance with approved data RBHA 23.1541, .1555 25.1541, .1555 |  |  |  |
| 8.3 | Is the installation of the pressurization system in accordance with related approved data RBHA 21.33 23.841 25.841 |  |  |  |
| 8.4 | Do the pressure relief valves automatically limit the positive pressure differential to the limits established by the approved data RBHA 23.841 25.841 |  |  |  |
| 8.5 | Do the reverse pressure differential relief valves limit the negative pressure differential to the limits established by the approved data RBHA 23.841 25.841 |  |  |  |
| 8.6 | Is the regulator for maintaining the required internal pressures and airflow rates installed and placarded in accordance with the approved data RBHA 23.841 25.841 |  |  |  |
| 8.7 | Are the instruments to indicate to the pilot the pressure differential, the absolute pressure in the cabin and the rate of change of the absolute pressure marked and placarded in accordance with the approved data RBHA 23.841, .1543 25.841, .1543 |  |  |  |
| 8.8 | Are warning devices and placards provided to indicate when the approved pressure differential and absolute cabin pressure limits are exceeded RBHA 23.841 25.841 |  |  |  |
| 8.9 | Are all pressurization system warning placards in accordance with approved data RBHA 23.841 25.841 |  |  |  |
| 8.10 | Does each door and emergency exit operate properly after the pressurization flight test have been completed RBHA 23.843 25.843 |  |  |  |
| 8.11 | Are combustion heaters of an approved type and installed in accordance with approved data RBHA 23.859 25.859 |  |  |  |
| 8.12 | Are engine exhaust heaters installed in accordance with approved data RBHA 23.1125 25.833, .1125 |  |  |  |

| 9.0 FIRE PROTECTION – COMPARTMENT INTERIORS | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 9.1 | Are the materials used for compartment interiors in accordance with approved data RBHA 23.853 25.853 |  |  |  |
| 9.2 | Does each towel, paper, and waste receptacle have a means for containing possible fires RBHA 25.853 |  |  |  |
| 9.3 | Is there at least one hand fire extinguisher for use by the flight crew members RBHA 25.853 |  |  |  |
| 9.4 | Are the required number of hand fire extinguishers located in the passenger compartments RBHA 25.853 |  |  |  |
| 9.5 | Is the location of each hand fire extinguisher plainly marked RBHA 23.1561 25.1561 |  |  |  |
| 9.6 | Are compartments where smoking is to be prohibited so placarded RBHA 25.853 |  |  |  |
| 9.7 | Are controls, wiring, fluid lines, equipment or accessories whose damage or failure would affect safe operation, protected so that they cannot be damaged by cargo or baggage, and that their breakage or failure will not create a fire hazard RBHA 25.855 |  |  |  |
| 9.8 | Has a means been provided to prevent cargo or baggage from interfering with the functioning of the fire-protective installation for the compartments RBHA 25.855 |  |  |  |
| 9.9 | Are the sources of heat within the compartment shielded and insulated to prevent igniting the cargo or baggage RBHA 25.855 |  |  |  |
| 9.10 | Are the combustion heater fire zones protected from fire RBHA 23.859 25.859 |  |  |  |
| 9.11 | Are the ventilating and combustion air ducts, adjacent to the heater of fire proof material installed in accordance with approved data RBHA 25.859 |  |  |  |
| 9.12 | Do the heater installation fuel drains permit safe drainage clear of the aircraft RBHA 25.859 |  |  |  |
| 9.13 | Is a means provided to prevent the ignition, by any equipment, of flammable fluids or vapors resulting from the leakage of fluid systems or to control any fire resulting from the ignition RBHA 25.863 |  |  |  |

| 10.0 POWERPLANT INSTALLATIONS | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 10.1 | GENERAL |  |  |  |
| 10.1.1 | Is (are) the engine(s) type certificated RBHA 23.903 25.903 | TYPE CERTIFICATE NO. |  |  |  |
| 10.1.2 | Is (are) the propeller(s) type certificated RBHA 23.905 25.905 | TYPE CERTIFICATE NO. |  |  |  |
| 10.1.3 | Are the powerplant components and accessories installed in accordance with approved data RBHA 23.901 25.901 |  |  |  |
| 10.1.4 | Does a ground operational test show that all powerplant components and accessories are operating satisfactorily RBHA 23.901 25.901 |  |  |  |
| 10.1.5 | Is a means provided to allow the close examination of each part requiring recurring inspection, adjustments for proper alignment and function, or lubrication RBHA 23.611, .901 25.611, .901 |  |  |  |
| 10.1.6 | Are major components of the powerplant installation electrically bonded to other parts of the airplane RBHA 25.901 |  |  |  |
| 10.1.7 | Are any self-locking nuts used on any bolt, subject to rotation in operation RBHA 23.607 25.607 |  |  |  |
| 10.1.8 | Is the radial clearance between the propeller tip and the aircraft structure at least one inch RBHA 23.925 25.925 |  |  |  |
| 10.1.9 | Is the longitudinal clearance between the propeller blades or cuffs and stationary part of the aircraft at least one-half inch RBHA 23.925 25.925 |  |  |  |
| 10.1.10 | Are propeller deicing provisions installed in accordance with approved data RBHA 23.901 25.901, .929 |  |  |  |
| 10.1.11 | Are propeller deicing controls identified and marked with respect to their operation RBHA 23.1555 25.1555 |  |  |  |
| 10.2 | FUEL SYSTEM |  |  |  |
| 10.2.1 | Is the fuel system installed in accordance with approved data RBHA 23.951 25.951 |  |  |  |
| 10.2.2 | Does a ground operational test indicate that the fuel system operates satisfactorily RBHA 23.951 25.951 |  |  |  |
| 10.2.3 | Are the fuel tanks constructed, installed and sealed in accordance with approved data RBHA 23.963 25.963 |  |  |  |
| 10.2.4 | Are the spaces adjacent to the fuel tanks ventilated and provided with drain holes RBHA 23.967 25.967 |  |  |  |

| 10.0 POWERPLANT INSTALLATIONS (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 10.2 | FUEL SYSTEM (Continued) |  |  |  |
| 10.2.5 | Does each tank have a positive locking drain that allows the complete drainage of the fuel tank sump RBHA 25.971 |  |  |  |
| 10.2.6 | Does the fuel tank sump drain discharge clear of the airplane RBHA 25.971 |  |  |  |
| 10.2.7 | Does the fuel system have a chamber or sediment bowl located so that water will drain to it from all parts of the fuel tank RBHA 23.97 |  |  |  |
| 10.2.8 | Can the fuel tank expansion space be filled with the airplane in the normal ground attitude RBHA 23.969 25.969 |  |  |  |
| 10.2.9 | Is the chamber or sediment bowl accessible for drainage RBHA 23.971 |  |  |  |
| 10.2.10 | Is each fuel tank filler connection installed in a manner which will prevent the entrance of fuel into any part of the airplane other than the tank RBHA 23.973 25.973 |  |  |  |
| 10.2.11 | Is each recessed fuel tank filler connection that can retain any appreciable quantity of fuel, provided with a drain that discharges clear of the airplane RBHA 23.973 25.973 |  |  |  |
| 10.2.12 | Is each fuel filler cover marked on or near, with the word “fuel,” the minimum fuel grade or designation approved for the engines and the usable fuel tank capacity RBHA 23.973,.1557 25.973,.1557 |  |  |  |
| 10.2.13 | Does each filler cap provide a fuel tight seal RBHA 23.973 25.973 |  |  |  |
| 10.2.14 | Is there any point in any fuel vent line where moisture can accumulate with the airplane in the ground attitude or level flight attitude RBHA 23.975 25.975 |  |  |  |
| 10.2.15 | Are the vent and drain line outlets located in a position where the discharge of fuel or fumes would not constitute a fire hazard or allow fumes to enter personnel compartments RBHA 23.975 25.975 |  |  |  |
| 10.2.16 | Are the fuel strainers accessible for inspection and cleaning RBHA 23.977 25.977 |  |  |  |
| 10.2.17 | Does an operational check of each pressure fueling connection show it to be operating satisfactorily RBHA 25.979 |  |  |  |
| 10.2.18 | Do the emergency or auxiliary fuel pumps function in accordance with the placards located at the controls RBHA 23.991 25.911 |  |  |  |

| 10.0 POWERPLANT INSTALLATIONS (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 10.2 | FUEL SYSTEM (Continued) |  |  |  |
| 10.2.19 | Are the fuel lines installed and supported to prevent excessive vibration and motion due to fuel pressure and accelerated flight conditions RBHA 23.993 25.993 |  |  |  |
| 10.2.20 | Do fuel lines, connected to components of the airplane between which relative motion could exist, have provisions for flexibility RBHA 23.993 25.993 “ |  |  |  |
| 10.2.21 | Does each fuel valve have positive stops or suitable index provisions in the “on” and “off” positions RBHA 23.995 25.995 |  |  |  |
| 10.2.22 | Can the drainage of the fuel system be accomplished by the use of fuel strainer and fuel tank sump drains with the airplane in the normal ground attitude RBHA 23.999 25.999 |  |  |  |
| 10.2.23 | Does a ground operational test indicate that the fuel jettisoning system operates satisfactorily RBHA 25.1001 |  |  |  |
| 10.3 | OIL SYSTEM |  |  |  |
| 10.3.1 | Is the oil system installed in accordance with the approved data RBHA 23.1011 25.1011 |  |  |  |
| 10.3.2 | Can the oil tank expansion space be filled with the airplane in the normal ground attitude RBHA 23.1013 25.1013 |  |  |  |
| 10.3.3 | Is each recessed oil tank filler connection that can retain any appreciable quantity of oil have a drain that discharges clear of the airplane RBHA 23.1013 25.1013 |  |  |  |
| 10.3.4 | Is each oil tank filler marked with the word “oil” and the oil capacity RBHA 23.1013,.1577 25.1013,.1557 |  |  |  |
| 10.3.5 | Does each filler cap provide an oil-tight seal RBHA 23.1013 25.1013 |  |  |  |
| 10.3.6 | Are the oil lines and oil tank vents routed so that condensed water vapor that might freeze and obstruct the line, cannot accumulate at any point RBHA 23.1013,.1017 25.1013, .1017 |  |  |  |
| 10.3.7 | Are the oil lines installed and supported to prevent excessive vibration and motion due to oil pressure and accelerated flight conditions RBHA 23.1017 25.1017 |  |  |  |
| 10.3.8 | Do oil lines, connected to components of the airplane between which relative motion could exist, have provisions for flexibility RBHA 23.1017 25.1017 |  |  |  |
| 10.3.9 | Is there at least one accessible oil drain which allows the safe drainage of the entire oil system, and is provided with a positive locking means in the closed position RBHA 23.1021 25.1021 |  |  |  |

| 10.0 POWERPLANT INSTALLATIONS (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 10.3 | OIL SYSTEM (Continued) |  |  |  |
| 10.3.10 | Does each oil valve have positive stops or suitable index provisions in the “on” and “off” positions RBHA 25.1025 |  |  |  |
| 10.3.11 | Does a ground operational test show that propeller feathering can be accomplished with the amount of trapped oil in the oil tank RBHA 23.1027 25.1027 |  |  |  |
| 10.4 | INDUCTION SYSTEM |  |  |  |
| 10.4.1 | Are all units of the engine air induction system, including icing protection and induction system screens, fabricated and installed in accordance with approved data RBHA 23.1091 25.1091 |  |  |  |
| 10.4.2 | Does the carburetor air preheater installation allow the inspection of exhaust manifold parts that it surrounds, and the critical parts of preheater itself RBHA 23.1101 25.1101 |  |  |  |
| 10.4.3 | Are drains for induction system ducts installed in accordance with approved data, and do they discharge in a location which will not cause a fire hazard RBHA 23.1103 25.1103 |  |  |  |
| 10.5 | EXHAUST SYSTEM |  |  |  |
| 10.5.1 | Are exhaust system components constructed and installed in accordance with approved data RBHA 23.1121 25.1121 |  |  |  |
| 10.5.2 | Are there parts of the airplane that hot exhaust gases could strike or that could be subjected to high temperatures from exhaust system parts constructed of fireproof material or shielded by a fireproof material RBHA 23.1121 25.1121 |  |  |  |
| 10.5.3 | Are exhaust gases discharged near any flammable fluid vent or drain RBHA 23.1121 25.1121 |  |  |  |
| 10.5.4 | Is each exhaust manifold supported to withstand any vibration and inertia load to which it may be subjected RBHA 23.1123 25.1123 |  |  |  |
| 10.5.5 | Has a means been provided for the inspection of critical parts of the exhaust heat exchangers RBHA 23.1125 25.1125 |  |  |  |
| 10.5.6 | Are the exhaust driven turbo supercharger installations in accordance with approved data RBHA 23.1127 25.1127 |  |  |  |
| 10.5.7 | Have adequate provisions been made for the inspection, maintenance, and servicing of the turbo supercharger RBHA 23.1127 25.1127 |  |  |  |

| 10.0 POWERPLANT INSTALLATIONS (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 10.6 | POWERPLANT CONTROLS AND ACCESSORIES |  |  |  |
| 10.6.1 | Are the powerplant controls constructed, located, installed, adjusted and marked in accordance with approved data RBHA 23.1141 25.1141 |  |  |  |
| 10.6.2 | Is there a means to prevent propeller feathering by movement of the propeller pitch or speed control to the feathering position during normal operation RBHA 23.1151 25.1153 |  |  |  |
| 10.6.3 | Do the reverse thrust controls have a positive lock or stop at the flight idle position and required a separate an distinct operation to displace the control from the forward thrust position RBHA 25.1155 |  |  |  |
| 10.6.4 | Are the fuel jettisoning system controls located apart from any fire extinguisher control or other control used to combat fire, and are guards provided to prevent inadvertent operation RBHA 25.1161 |  |  |  |
| 10.6.5 | Are all engine mounted accessories installed in accordance with approved data RBHA 23.1163 25.1163 |  |  |  |
| 10.6.6 | Is the electrical equipment that is subject to arcing or sparking installed in a location to minimize the probability of contact with any flammable fluids or vapors RBHA 23.1163 25.1163 |  |  |  |
| 10.6.7 | Are the magneto ground wires that lie on the engine side of the fire wall installed, located, or protected, to minimize the probability of simultaneous failure of two or more wires due to mechanical damage, electrical faults, or other cause RBHA 23.1165 25.1165 |  |  |  |
| 10.6.8 | Are ground wires for any engine, which are routed through the fire zone of another engine, fire proof RBHA 25.1165 |  |  |  |
| 10.7 | POWERPLANT FIRE PROTECTION |  |  |  |
| 10.7.1 | Are all tanks, lines, and fittings which contain flammable fluids or gases in a designated fire zone constructed, installed, and secured in accordance with approved data RBHA 23.1183 25.1185 |  |  |  |
| 10.7.2 | Can complete drainage and discharge of each part of each designated fire zones be accomplished to minimize the hazard resulting from the failure of malfunctioning of any component containing flammable fluids RBHA 25.1187 |  |  |  |
| 10.7.3 | Is each designated fire zone ventilated to prevent the accumulation of flammable vapors RBHA 25.1187 |  |  |  |

| 10.0 POWERPLANT INSTALLATIONS (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 10.7 | POWERPLANT FIRE PROTECTION (Continued) |  |  |  |
| 10.7.4 | Are the shut-off valves and controls installed and marked in accordance with approved data RBHA 23.1189 25.1189 |  |  |  |
| 10.7.5 | Are firewalls and shrouds constructed and installed in accordance with approved data RBHA 23.1191 25.1191 |  |  |  |
| 10.7.6 | Are all openings in firewalls and shrouds provided with close fitting fireproof or fire-resistant grommets, brushings, or firewall fittings RBHA 23.1191 25.1191 |  |  |  |
| 10.7.7 | Is each part of the cowling provided with a means for rapid and complete drainage in the normal ground and flight attitudes RBHA 23.1193 25.1193 |  |  |  |
| 10.7.8 | Is the cowling and nacelle constructed and installed in accordance with the approved data RBHA 23.1193 25.1193 |  |  |  |
| 10.7.9 | Are fire extinguishing systems, which are provided for designated fire zones installed in accordance with approved data RBHA 23.1195 25.1195 |  |  |  |
| 10.7.10 | Are visual discharge indicators provided at the discharge end of each discharge line of the fire extinguishing system RBHA 25.1199 |  |  |  |
| 10.7.11 | Are all powerplant fire or overheat detector systems installed in accordance with approved data RBHA 25.1203 |  |  |  |
| REMARKS |

| 11.0 EQUIPMENT |
| --- |
| Due to the differences in the minimum equipment requirements of RBHA 23 and 25, the following list of instruments and equipment items is provided as a means of recording the inspection of these items. The RBHA requiring the particular item is indicated beside the item in the applicable RBHA column. The answers to the following questions should be noted in the appropriate column. |
| Is the item installed and marked in accordance with approved data RBHA 23.1301, .1541 25.1301, .1541 |
| Does a ground operational check show that the item operates satisfactorily RBHA 23.1301, .1309 25.1301, .1309 |
| Is action required as a result of this inspection |
| 11.1 FLIGHT AND NAVIGATIONAL INSTRUMENTS – RBHA 23.1303 25.1303 |
| ITEM | RBHA | A. | B. | C. |
|  | 23 | 25 |  |  |  |
|  | Airspeed indicator | X | X |  |  |  |
|  | Altimeter | X |  |  |  |  |
|  | Altimeter (Sensitive or precision0 |  | X |  |  |  |
|  | Clock (Sweep second pointer) |  | X |  |  |  |
|  | Free air temperature indicator |  | X |  |  |  |
|  | Rate-of-turn indicator (Gyroscopically with integral bank or slip indicator) |  | X |  |  |  |
|  | Bank and pitch indicator (Gyroscopically stabilized) |  |  |  |  |  |
|  | Magnetic direction indicator | X | X |  |  |  |
|  | Rate of climb |  | X |  |  |  |
|  | Gyroscopic direction indicator (Directional gyro or equivalent) |  | X |  |  |  |
|  | Machmeter |  | X |  |  |  |
|  | Speed warning device |  | X |  |  |  |
|  | Oxygen quantity indicator |  | X |  |  |  |
|  | Hydraulic pressure indicator |  | X |  |  |  |
|  | Electrical power indicators | X | X |  |  |  |
|  | Landing gear position indicator | X | X |  |  |  |
|  | Wing flap position indicator | X | X |  |  |  |
|  | Trim position indicator | X | X |  |  |  |
|  | Differential pressure indicator |  | X |  |  |  |
|  | Cabin absolute pressure indicator |  | X |  |  |  |
|  | Rate-of-change of cabin absolute pressure |  | X |  |  |  |

| 11.0 EQUIPMENT (Continued) |
| --- |
| Is the item installed and marked in accordance with approved data RBHA 23.1301, .1541 25.1301, .1541 |
| Does a ground operational check show that the item operates satisfactorily RBHA 23.1301, .1309 25.1301, .1309 |
| Is action required as a result of this inspection |
| 11.2 POWERPLANT INSTRUMENTS – RBHA 23.1305 25.1305 |
| ITEM | RBHA | A. | B. | C. |
|  | 23 | 25 |  |  |  |
|  | Carburetor air temperature indicator |  | X |  |  |  |
|  | Manifold pressure indicator | X | X |  |  |  |
|  | Cylinder head temperature indicator | X | X |  |  |  |
|  | Fuel pressure indicator | X | X |  |  |  |
|  | Fuel pressure warning device |  | X |  |  |  |
|  | Fuel flowmeter (turbine engine) |  | X |  |  |  |
|  | Fuel mixture indicator (reciprocating engine without auto alt. Mixture control) |  | X |  |  |  |
|  | Gas temperature indicator (turbine) |  | X |  |  |  |
|  | Fuel quantity indicator | X | X |  |  |  |
|  | Oil pressure indicator | X | X |  |  |  |
|  | Oil pressure warning |  | X |  |  |  |
|  | Oil quantity indicator | X | X |  |  |  |
|  | Oil temperature indicator | X | X |  |  |  |
|  | Tachometer | X | X |  |  |  |
|  | Fire warning indicator |  | X |  |  |  |
|  | Thrust indicator |  | X |  |  |  |
|  | Torque indicator (turbo prop) |  | X |  |  |  |
|  | Power output indicator (recip.) |  | X |  |  |  |
|  | Propeller blade position indicator |  | X |  |  |  |
|  | Reverse thrust indicator |  | X |  |  |  |

| 11.0 EQUIPMENT (Continued) |
| --- |
| Is the item installed and marked in accordance with approved data RBHA 23.1301, .1541 25.1301, .1541 |
| Does a ground operational check show that the item operates satisfactorily RBHA 23.1301, .1309 25.1301, .1309 |
| Is action required as a result of this inspection |
| 11.3 MISCELLANEOUS EQUIPMENT – RBHA 23.1307 25.1307 |
| ITEM | RBHA | A. | B. | C. |
|  | 23 | 25 |  |  |  |
|  | Approved seat for each occupant |  | X |  |  |  |
|  | Approved safety belt for each occupant | X | X |  |  |  |
|  | Adequate electrical energy source | X | X |  |  |  |
|  | Two-way radio communication |  | X |  |  |  |
|  | Radio navigation system |  | X |  |  |  |
|  | Windshield wiper or equivalent |  | X |  |  |  |
|  | Ignition switch (es) | X | X |  |  |  |
|  | Portable fire extinguisher |  | X |  |  |  |
|  | Master switch | X | X |  |  |  |
|  | Anti-Collision light | X7 | X7 |  |  |  |
|  | Electric protective devices | X | X |  |  |  |
| REMARKS |
| 7 Night operational requirement |

| 12.0 ELECTRICAL SYSTEM | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 12.1 | Is the electrical system installed in accordance with approved data RBHA 23.1351 25.1351,.1309 |  |  |  |
| 12.2 | Does a ground operational test show that the electrical system adequately performs its intended function RBHA 23.1351 25.1351,.1309 |  |  |  |
| 12.3 | Is the electrical system protected from fuel, oil, water, other detrimental substances and mechanical damage RBHA 23.1351 25.1351 |  |  |  |
| 12.4 | Are all electrical control devices operated by a crew member marked or placarded in accordance with approved date RBHA 23.1351,.1555 25.1351,.1555 |  |  |  |
| 12.5 | Are electrical system components located in wheel wells protected to prevent a malfunction or failure due to water, slush, ice, or any material which may be thrown by a tire RBHA 23.1351 25.1351 |  |  |  |
| 12.6 | Is the battery installation provided with adequate drainage and ventilation, and enclosed so that no corrosive fluids or gases may damage the surrounding structure or essential equipment RBHA 23.1353 25.1353 |  |  |  |
| 12.7 | Are instrument lights installed in accordance with approved data RBHA 23.1381 25.1381 |  |  |  |
| 12.8 | Are landing lights installed in accordance with approved data RBHA 23.1383 25.1383 |  |  |  |
| 12.9 | Are the position lights installed in accordance with approved data RBHA 23.1385 through .1297 25.1383 through .1297 |  |  |  |
| 12.10 | Is the riding light installation in accordance with approved data RBHA 23.1399 25.1399 |  |  |  |
| 12.11 | Is the anticollision light installation in accordance with approved data RBHA 23.1401 25.1401 |  |  |  |
| 12.12 | Are parts which are electrically insulated from the basic airframe connected to it through lightning arrestors RBHA 25.1369 |  |  |  |
| 13.0 SAFETY EQUIPMENT |  |  |  |
| 13.1 | Are the safety equipment release controls, such as automatic liferaft release readily accessible to the crew RBHA 23.1411 25.1411 |  |  |  |
| 13.2 | Are the emergency equipment items located in an obvious location which is readily accessible RBHA 23.1411 25.1411 |  |  |  |
| 13.3 | Are the emergency equipment items stowed in a manner that provides protection from inadvertent damage RBHA 23.1411 25.1411 |  |  |  |
| 13.4 | Are liferafts installed in accordance with approved data RBHA 23.1411 25.1411 |  |  |  |

| 14.0 MISCELLANEOUS EQUIPMENT | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 14.1 | ELECTRONIC SYSTEM |  |  |  |
| 14.1.1 | Is the electronic system installed in accordance with approved data RBHA 23.1431,.1309 25.1431,.1309 |  |  |  |
| 14.1.2 | Does a ground operational check show that the electrical system adequately performs its intended function RBHA 23.1309,.1431 25.1309,.1431 |  |  |  |
| 14.1.3 | Is the electronic system protected from damage by fuel, oil, water, other detrimental substances and mechanical damage RBHA 23.1309,.1431 25.1309,.1431 |  |  |  |
| 14.1.4 | Are all electronic control devices operated by a crew member marked or placarded in accordance with approved data RBHA 23.1431,.1555 25.1431,.1555 |  |  |  |
| 14.1.5 | Are the electronic system controls and wiring installed so that the operation of any one unit or system of units will not adversely affect the simultaneous operation of any other unit or systems of units within the aircraft RBHA 23.1431 25.1431 |  |  |  |
| 14.1.6 | Are the electronic units properly ventilated RBHA 23.1431 25.1431 |  |  |  |
| 14.1.7 | Are shock mounted units provided with adequate clearance between other units or aircraft parts to prevent damage or malfunction RBHA 23.1431 25.1431 |  |  |  |
| 14.2 | HYDRAULIC – PNEUMATIC – VACUUM SYSTEMS |  |  |  |
| 14.2.1 | Is the hydraulic system installed in accordance with the approved data RBHA 23.1435 25.1435 |  |  |  |
| 14.2.2 | Does a ground operational test show that the hydraulic system adequately performs its intended functions RBHA 23.1301,.1435 25.1301,.1435 |  |  |  |
| 14.2.3 | Is each hydraulic line, fitting and component installed and supported to prevent excessive vibration and damage due to inertia loads RBHA 23.1435 25.1435 |  |  |  |
| 14.2.4 | Has a flexible means been used to connect points in the hydraulic system between which relative motion or differential vibration exists RBHA 23.1435 25.1435 |  |  |  |
| 14.2.5 | Is each element of the hydraulic system protected from abrasion, corrosion and mechanical damage RBHA 23.1435 25.1435 |  |  |  |
| 14.2.6 | Are the hydraulic reservoirs and accumulators installed in accordance with approved data RBHA 23.1435 25.1435 |  |  |  |

| 14.0 MISCELLANEOUS EQUIPMENT (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 14.2 | HYDRAULIC – PNEUMATIC – VACUUM SYSTEMS (Continued) |  |  |  |
| 14.2.7 | Are the hydraulic system controls and components labeled as to their identification, function or operating limitations, or any applicable combination of these factors RBHA 23.1309 25.1309 |  |  |  |
| 14.2.8 | Is the pneumatic system installed in accordance with approved data RBHA 23.1309 25.1309 |  |  |  |
| 14.2.9 | Does a ground operation test show that the pneumatic system adequately performs its intended function RBHA 23.1309 25.1309 |  |  |  |
| 14.2.10 | Is each pneumatic system line, fitting and component installed and supported to prevent excessive vibration and damage due to inertia loads RBHA 23.1309 25.1309 |  |  |  |
| 14.2.11 | Is each element of the pneumatic system protected from abrasion, corrosion and mechanical damage RBHA 23.1309 25.1309 |  |  |  |
| 14.2.12 | Are the pneumatic system controls and components labeled as to their identification, function or operating limitations or any applicable combination of these factors RBHA 23.1301,.1309 25.1301,.1309 |  |  |  |
| 14.2.13 | Are the vacuum air system units, components lines and connections installed in accordance with approved data RBHA 25.1433 |  |  |  |
| 14.3 | OXYGEN SYSTEM |  |  |  |
| 14.3.1 | Is the oxygen system installed in accordance with approved data RBHA 25.1441 |  |  |  |
| 14.3.2 | Does a ground operational test show that the oxygen system adequately performs its intended function RBHA 25.1441 |  |  |  |
| 14.3.3 | Are any oxygen equipment or lines located within a designated fire zone RBHA 25.1451 |  |  |  |
| 14.3.4 | Are oxygen lines and equipment protected from heat that may be generated in, or escape from, any designated fire zone RBHA 25.1451 |  |  |  |
| 14.3.5 | Are the oxygen system components and lines installed so that escaping oxygen cannot cause ignition of grease, fluids, or vapor accumulations that are present in normal operation or as a result of failure or malfunction of any system RBHA 25.1451 |  |  |  |
| 14.3.6 | Are the oxygen system controls and components labeled as to their identification , function or operating limitations or any applicable combination of these factors RBHA 23.1301 25.1301 |  |  |  |

| 14.0 MISCELLANEOUS EQUIPMENT (Continued) | Yes | No | Action Req. |
| --- | --- | --- | --- |
| 14.3 | OXYGEN SYSTEM (Continued) |  |  |  |
| 14.3.7 | Are oxygen pressure tanks and lines between tanks and the shutoff means protected from unsafe temperatures, and (b) located where the probability and hazards of rupture in a crash landing are minimized RBHA 25.1453 |  |  |  |
| 14.3.8 | Is each oxygen system line, fitting and component installed and supported to prevent excessive vibration and damage due to inertia loads RBHA 23.1309 25.1309 |  |  |  |
| 14.3.9 | Is each element of the oxygen system protected from abrasion, corrosion and mechanical damage RBHA 23.1309 25.1309 |  |  |  |
| 14.3.10 | Is the portable oxygen equipment readily accessible to the crew members RBHA 25.1443 |  |  |  |
| 14.4 | MISCELLANEOUS FLUID DRAINS |  |  |  |
| 14.4.1 | Where fluids subject to freezing are drained overboard in flight or during ground operations, are these drains located to prevent the formation of ice on the airplane RBHA 25.1455 |  |  |  |
| 15.0 AIRCRAFT IDENTIFICATION AND MARKING |  |  |  |
| 15.1 | Is the manufacturer’s identification plate fireproof, and attached in an accessible location where it will not likely be defaced during normal service or be lost or destroyed in the event of an accident RBHA 45.11 |  |  |  |
| 15.2 | Does the manufacturer’s identification plate contain the data required by RBHA 45.13 RBHA 45.11 |  |  |  |
| 15.3 | Are aircraft nationality and registration marks in accordance with approved data RBHA 45.21 through 45.31 |  |  |  |
| 16.0 SOFTWARE SYSTEM |  |  |  |
| 16.1 | Are all Non FLS clearly identified? For this purpose, there are two kinds: (1) software and hardware is identified as an unique part number or (2) both have separated part number. Booth identification are physical. RBHA 25.1301 |  |  |  |
| 16.2 | Are all FLS clearly identified? For this purpose, there are three kinds: (1) software identified electronically on the display, or (2) software and hardware are identified separately on the placard or (3) software database identified electronically on the display. RBHA 25.1301 |  |  |  |
| 16.3 | Are the following equipments installed and clearly identified? MAU (3), SPDA (2), FADEC (engine (2) + APU (1)), MCDU (2), MRC (2), Smart Probe (4),CMC (1), DVDR (2) and ACE (6). RBHA 25.1301 |  |  |  |
| 16.4 | Are the software part number and/or version installed in the equipments clearly identified on label or placard (not field loadable software)? RBHA 25.1301 |  |  |  |
| 16.5 | Are the software part number and/or version installed inside equipments with field loadable software clearly identified via electronic part number? RBHA 25.1301 |  |  |  |
| 16.0 | SOFTWARE SYSTEM (Continued) |  |  |  |
| 16.6 | Are the software part number and/or version installed inside APM clearly identified on CMS? RBHA 25.1301 |  |  |  |
| 16.7 | Inside the MAU there are some LRU with software installed. Are the software part number and/or version of each LRU clearly identified in the master drawing list? RBHA 25.1301 |  |  |  |
| 16.8 | Is the software part number and/or version of Electronic Checklist Database clearly identified on the MFD and is it match with QRH version? RBHA 25.1301 |  |  |  |
| 16.9 | Is there a critical FLS Database installed and clearly physically or electronically identified on specific equipment on board on aircraft? RBHA 25.1301 |  |  |  |
| REMARKS |